## Slide 1
Introduction to Programming (II)
楊舜仁
Computer System and Assembly

## Slide 2: References
李哲榮教授上課投影片&講義
J.Glenn Brookshear "Computer Science - AN OVERVIEW", Addison-Wesley
http://www.cs.virginia.edu/~evans/cs216/guides/x86.html
http://www.nasm.us/pub/nasm/releasebuilds/2.09.02/win32/nasm-2.09.02-win32.zip
http://eli.thegreenplace.net/2011/02/04/where-the-top-of-the-stack-is-on-x86/
http://www.ibiblio.org/gferg/ldp/GCC-Inline-Assembly-HOWTO.html
http://ccckmit.wikidot.com/as:inlinec
  陳鍾誠 (2010年10月11日)，(網頁標題) 組合語言 — 在 C 語言當中內嵌組合語言，(網站標題) 陳鍾誠的網站，取自http://ccckmit.wikidot.com/as:inlinec ，網頁修改第 0 版。

## Slide 3: Outline
From C code to assembly code to machine code
From logic circuit to gate to semi-conductor
How to get assembly code?
From C to assembly code
Advanced syntaxes in assembly
  Pointers
  Arrays
  Function calls

## Slide 4: From C code to assembly code to machine code

## Slide 5: Computer system
Mother board (主機板)
Hard disk
(硬碟)
CPU (中央處理器)
Memory (記憶體)
ALU
(計算邏輯單元)
Registers
(暫存器)

## Slide 6: How is a program executed?
Mother board (主機板)
Hard disk
(硬碟)
CPU (中央處理器)
Memory (記憶體)
ALU
(計算邏輯單元)
Registers
(暫存器)
HelloWorld.c
Assembly code
Compiler
Assembler
Machine code
(Executable)
Machine code
(Executable)

## Slide 7: Computer Architecture
Central Processing Unit (CPU) or processor
  Arithmetic/Logic unit versus Control unit
  Registers
    General purpose
    Special purpose
Bus

## Slide 8: CPU and main memory connected via a bus

## Slide 9: Stored Program Concept
Early computers were not known for their flexibility—
  the steps that each device executed were built into the control unit as a part of the machine.
A breakthrough: A program can be encoded as bit patterns and stored in main memory.
  From there, the CPU can then extract the instructions and execute them.
  In turn, the program to be executed can be altered easily.

## Slide 10: Terminology
Machine instruction: An instruction (or command) encoded as a bit pattern recognizable by the CPU
Machine language: The set of all instructions recognized by a machine

## Slide 11: Machine Instruction Types
Data Transfer
  Copy data between CPU and memory/devices
  E.g., LOAD, STORE, device I/O,
Control
  Direct the execution of the program
  E.g., JUMP, BRANCH, JNE (conditional jump),
Arithmetic/Logic
  Use existing data values to compute a new value
  E.g., ADD, AND, OR, XOR, SHIFT, etc.

## Slide 12: Dividing values stored in memory

## Slide 13: Parts of a Machine Instruction
Op-code: Specifies which operation to execute
Operand: Gives more detailed information about the operation
  Interpretation of operand varies depending on op-code

## Slide 14: The composition of an instruction

## Slide 15: Decoding the instruction 35A7

## Slide 16: An encoded version of the instructions

## Slide 17: Program Execution
Controlled by two special-purpose registers
  Program counter: address of next instruction
  Instruction register: current instruction
Machine Cycle
  Fetch
  Decode
  Execute

## Slide 18: The program stored in main memory ready for execution

## Slide 19: Performing the fetch step of the machine cycle

## Slide 20: Performing the fetch step of the machine cycle (cont’d)

## Slide 21: The machine cycle

## Slide 22: Assembly language
A mnemonic (幫助記憶的詞句) system for representing machine instructions
  Mnemonic names for op-codes
  Identifiers: Descriptive names for memory locations, chosen by the programmer

## Slide 23: Program Example
Machine language 156C 166D 5056 30CE C000
Assembly language LD R5, Price LD R6, ShippingCharge ADDI R0, R5 R6 ST R0, TotalCost HLT

## Slide 24: Assembly Language Characteristics
One-to-one correspondence between machine instructions and assembly instructions
  Programmer must think like the machine
Inherently machine-dependent
Converted to machine language by a program called an assembler

## Slide 25: From logic circuit to gate to semi-conductor

## Slide 26: Instruction execution
Data transfer: load, store, …
Control: jump, jump-equal, …
  Change the value of program counter (PC)
Arithmetic/Logic: add, and, shift, …
=> All implemented using logic circuits

## Slide 27: Boolean Operations
Inside today’s computers information is encoded as patterns of 0s and 1s.
  bit 0: false
  bit 1: true
Boolean Operation: An operation that manipulates one or more true/false values
  AND
  OR
  XOR (exclusive or)
  NOT

## Slide 28: The Boolean operations AND, OR, and XOR (exclusive or)

## Slide 29: Gates
Gate: A device that computes a Boolean operation
  Often implemented as (small) electronic circuits
  Provide the building blocks from which computers are constructed

## Slide 30: A pictorial representation of AND, OR, XOR, and NOT gates as well as their input and output values

## Slide 31: Boolean functions
Almost all binary operations of computers can be carried out by logic gates
Example: One bit adder
  Two inputs and two outputs (S: sum, C: carry out)
A: input 1
B: input 2
S: output 1
C: output 2

## Slide 32: Implementation of one bit adder
The truth table of an one-bit adder
Compare it to the truth table of Boolean function AND, OR, XOR, NOT
  S = A .XOR. B
  C = A .AND. B
A | B | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 33: 4 bit parallel adder

## Slide 34: Circuit gates
Can we flip the switches without hands?
A
B
AND gate
A
B
OR gate
A
NOT gate
A
B
A
B
XOR gate

## Slide 35: Electronic switch: Transistors for logic gates
CMOS

## Slide 36: Integrated circuit (IC)
An electronic circuit consisted of transistors and other components in the thin substrate of semiconductor material.
Also known as IC, microchip, or chip.
Invented by Jack Kilby and Robert Noyce
  2000 Nobel Prize in Physics
Erasable Programmable Read-Only Memory (EPROM) integrated circuits.

## Slide 37: Discrimination
Name | Example | Meaning
Boolean operations | AND, OR, XOR, NOT | Math (logic) concept
Logic gate | AND gate, OR gate, XOR gate | Physical device implementing Boolean operations
Bitwise operators | &, ¦, ^, ~, >>, << | High level language syntax to process bits

## Slide 38: How to get Assembly code?

## Slide 39: How to get the assembly code?
In the terminal, use gcc -S ex1.c to get the assembly code of ex1.c
In today’s lecture, we use x86 CPU and intel style’s assembly
  gcc -S -masm=intel ex1.c
To generate executable, you can compile the assembly code directly
  gcc ex1.s

## Slide 40: How to get the assembly code?
To get cleaner and thus more understandable assembly code, we may compile as follows
  gcc -S -masm=intel -fno-common -fno-asynchronous-unwind-tables -mno-stack-arg-probe -mpush-args -mno-accumulate-outgoing-args ex1.c

## Slide 41: From C to Assembly code

## Slide 42: Example 1: assignment 1
C code
Assembly code
int a;
int main(void){
a = 3;
}
mov DWORD PTR _a, 3

## Slide 43: MOV instruction
MOV is an instruction in x86’s architecture
In example 1, destination is a memory address, named _a, and source is a constant value (3).
DWORD specifies the data size.
MOV destination, source
Type Specifier | Bytes addressed
BYTE | 1
WORD | 2
DWORD | 4
QWORD | 8

## Slide 44: Example 2: assignment 2
C code
Assembly code
int main(void){
int a;
a = 3;
}
mov DWORD PTR [esp+12], 3
What’s differences between ex1 and ex2?

## Slide 45: Registers in x86 CPU

## Slide 46: Indirect memory access
Register esp holds an address of memory.
[esp+12] is a memory address, whose cell is 12 bytes below the memory cell addressed [esp].
[esp]
[esp+04]
[esp+08]
[esp+12]
[esp+16]
Register esp
Memory
Address

## Slide 47: Stack
A stack is a data structure that has two operations: push and pop
  push adds an element to the collection;
  pop removes the last element that was added.
Elements are only allowed to be added and removed from the “top” of a stack
  First come last out

## Slide 48: Hardware supported stack in x86 CPU
x86 CPU has a hardware supported stack
  Two instructions: push and pop
  Register esp (stack pointer): point to the stack top
  Register ebp (base pointer): point to the stack base
Used for local variable storage during function execution and other purposes
  local variables used by subroutines are placed in memory on the stack.

## Slide 49: Stack manipulation for function execution
ESP
EBP
…
…
…
ESP
EBP
…
…
…
saved EBP
local variable 1
local variable 2
local variable n
…
Before the function is invoked
At the beginning of the function execution

## Slide 50: Global variable vs. local variable
Variable a in example 1 is a global variable, and in example 2 is a local variable.
 | Global variable | Local variable
Creation | Program starts | Function is called
Life time | Program stops | Function returns
Copies | Only one | The number of function called.
Address | In the data seg | In the stack
Accessible | Everywhere | Within the function

## Slide 51: Example 3: assignment 3
C code
Assembly code
int main(void){
int a, b;
b = a;
}
mov eax, DWORD PTR [esp+12]
mov DWORD PTR [esp+8], eax
eax is another register in x86 CPU
Notes: Continue the game,
Ask each student to have a number in hand.
Put a number in esp, for example, 20
Ask what is the number of in [esp+12], put that to eax
Ask the student in [esp+8] to have the same number

## Slide 52: Syntax of MOV
In the syntax of MOV, none of them are destination=mem and source=mem
  Why?
<mem> can be a direct address or an indirect address
A single b=a needs 2 instructions.
Valid MOV syntax
mov <reg>,<reg> mov <reg>,<mem> mov <mem>,<reg> mov <reg>,<const> mov <mem>,<const>
MOV destination, source

## Slide 53: Discrimination
Name | Example | Meaning
Variable | a, b, c | The high level naming of memory space.
Value | 1, 2, 3 | The value stored in the memory space.
Memory address | [21],[63], [D8] | The address of memory where data are stored.
Register | r1, r5, r10 | Temporary storage of data inside CPU.

## Slide 54: Example 4: Add
C code
Assembly code
int main(void){
int a, b, c;
c = a + b;
}
mov eax, DWORD PTR [esp+8]
mov edx, DWORD PTR [esp+12]
add eax, edx
mov DWORD PTR [esp+4], eax
eax, edx are registers in x86 CPU
Notes: Continue the game,
Ask each student to have a number in hand.
Put a number in esp, for example, 20
Ask what is the number of in [esp+8], put that to eax
Ask what is the number of in [esp+12], put that to edx
Perform add eax, edx
Ask the student in [esp+4] to have the number in eax

## Slide 55: ADD instruction
The add instruction adds together its two operands, storing the result in its first operand.
Ex: add BYTE PTR [var], 10
  add 10 to the single byte stored at memory address var
Ex: add eax, 10
  EAX ← EAX + 10
Valid add syntax
add <reg>,<reg> add <reg>,<mem> add <mem>,<reg> add <reg>,<con> add <mem>,<con>

## Slide 56: Example 5: If-else
C code
Assembly code
int main(void){
int a, b;
if (a>3) b++;
}
cmp DWORD PTR [esp+12], 3
jle L3
add DWORD PTR [esp+8], 1
L3:
leave
Notes: Continue the game,
Ask each student to have a number in hand.
Put a number in esp, for example, 20
Ask what is the number of in [esp+8], put that to eax
Ask what is the number of in [esp+12], put that to edx
Perform add eax, edx
Ask the student in [esp+4] to have the number in eax

## Slide 57: Cmp and jle instructions
cmp compares the values of the two specified operands, setting the condition codes in the machine status word.
  Machine status word is another register in x86 CPU
jle <label> jumps to the label if the machine status word shows “less than or equal to”

## Slide 58: Conditional jump
je <label> (jump when equal)
jne <label> (jump when not equal)
jz <label> (jump when last result was zero)
jg <label> (jump when greater than)
jge <label> (jump when greater than or equal to)
jl <label> (jump when less than)
jle <label> (jump when less than or equal to)

## Slide 59: Instruction pointer (IP)
The program (a list of instructions) is stored in memory.
Which instruction to be executed is specified by a special register, called instruction pointer.
  In some place, it is called “program counter” (PC).
Normally, IP increases 4 bytes (an instruction). But for jump <label>, it will become the address of the instruction after the label.
<label> represents a memory address.
Notes: Play the game that give 5 students the following instructions
模擬一下不同的執行
1.call ___main
2. cmp DWORD PTR [esp+12], 3
3. jle L3
4. add DWORD PTR [esp+8], 1
L3:
5. leave

## Slide 60: Example 6: while loop
C code
Assembly code
int main(void){
int a, b;
while(a<=3) b++;
}
jmp L2
L3:
add DWORD PTR [esp+12], 1
L2:
cmp DWORD PTR [esp+8], 3
jle L3
leave
Notes: Continue the game,
Ask each student to have a number in hand.
Put a number in esp, for example, 20
Ask what is the number of in [esp+8], put that to eax
Ask what is the number of in [esp+12], put that to edx
Perform add eax, edx
Ask the student in [esp+4] to have the number in eax

## Slide 61: jmp instruction
jmp <label> transfers program control flow to the instruction at the memory location indicated by the operand (<label>).
Instruction jmp is called “unconditional jump”

## Slide 62: Different implementation
The implementation is not unique.
int main(void){
int a, b;
while(a<=3) b++;
}
L3:
cmp DWORD PTR [esp+8], 3
jg L2
add DWORD PTR [esp+12], 1
jmp L3
L2:
leave

## Slide 63: Advanced syntaxes in assembly

## Slide 64: Example 7: pointer
C code
Assembly code
int main(void){
int a;
int *pa;
pa = &a;
}
lea eax, [esp+8]
mov DWORD PTR [esp+12], eax

## Slide 65: lea instruction
The lea (Load effective address) instruction places the address specified by its second operand into the register specified by its first operand.
  Note, the contents of the memory location are not loaded, only the effective address is computed and placed into the register.
  This is useful for obtaining a pointer into a memory region.

## Slide 66: Example 8: pointer 2
C code
Assembly code
int main(void){
int a;
int *pa;
pa = &a;
*pa = 3;
}
lea eax, [esp+8]
mov DWORD PTR [esp+12], eax
mov eax, DWORD PTR [esp+12]
mov DWORD PTR [eax], 3

## Slide 67
[esp]
[esp+04]
[esp+08] (a)
[esp+12] (pa)
Register esp
Memory
Address
Register eax
lea eax, [esp+8]
mov DWORD PTR [esp+12], eax
mov eax, DWORD PTR [esp+12]
mov DWORD PTR [eax], 3
3

## Slide 68: Example 9: array
C code
Assembly code
int main(void){
int a[3];
a[0] = 2;
a[1] = -6;
a[2] = 10000;
}
mov DWORD PTR [esp+4], 2
mov DWORD PTR [esp+8], -6
mov DWORD PTR [esp+12], 10000

## Slide 69: Array and pointer
Array | Pointer
A continuous space to store the data of the same data type | A space that stores the address of a specific type of data
a[2]: the third element in that continuous space | *(pa+2): the element that is 2 units away from the element pointed by pa
An array a is a “reference” of a space, which cannot be changed. | A pointer pa can change its content to point to other addresses.

## Slide 70: Example 10: function call
C code
Assembly (call foo)
int foo(int a){
return a+1;
}
int main(void){
foo(3);
}
mov DWORD PTR [esp], 3
call _foo

## Slide 71: C language calling convention
The calling convention is a protocol about how to call and return from functions.
Two instructions for function call and return
  Call: push the current code location onto the hardware supported stack; unconditional jump to the code location indicated by the label operand.
  Ret: pop the current code location from the hardware supported stack; unconditional jump to the popped code location.

## Slide 72: Recall: Hardware supported stack
x86 CPU has a hardware supported stack
  Two instructions: push and pop
  Register esp (stack pointer): point to the stack top
  Register ebp (base pointer): point to the stack base
Used for function calls
  Registers are saved on the stack.
  Subroutine parameters are passed on the stack, and
  local variables used by subroutines are placed in memory on the stack.

## Slide 73: The flow of a function call
Caller: the one who makes the function call
Callee: the called function
Caller calls the function
Callee starts the function
Callee performs the function
Callee returns
Caller restores

## Slide 74: Caller rules to call function
Before calling a function, push the contents of certain registers to the stack.
  The caller-saved registers are EAX, ECX, EDX.
To pass parameters to the subroutine, push them onto the stack before the call.
To call the function, use the call instruction.
  Instruction call pushes the return address on top of the parameters on the stack, and jumps to the function code.

## Slide 75: Callee rules to start a function
Push the value of EBP onto the stack, and copy the value of ESP into EBP
Allocate local variables by making space on the stack.
Push the values of the callee-saved registers that will be used by the function.
  The callee-saved registers are EBX, EDI, and ESI

## Slide 76: Function call memory layout (after the above two sets of rules)

## Slide 77: Callee rules to return
Leave the return value in EAX.
Restore the old values of any callee-saved registers (EDI and ESI) that were modified.
Deallocate local variables.
Before returning, restore the caller's base pointer value by popping EBP off the stack.
Return to the caller by executing a ret instruction.

## Slide 78: Caller rules to restore
Find the return value of function in the register EAX.
Remove the parameters from stack.
  This restores the stack to its state before the call was performed.
Pop off the contents of caller-saved registers (EAX, ECX, EDX) from the stack.
  The caller can assume that no other registers were modified by the callee.

## Slide 79: An example function definition that follows the callee rules
_myFunc PROC
  ; Subroutine Prologue (序言)
  push ebp ; Save the old base pointer value.
  mov ebp, esp ; Set the new base pointer value.
  sub esp, 4 ; Make room for one 4-byte local variable.
  push edi ; Save the values of registers that the function
  push esi ; will modify. This function uses EDI and ESI.
  ; (no need to save EBX)
(cont'd)

## Slide 80
  ; Subroutine Body
  mov eax, [ebp+8] ; Move value of parameter 1 into EAX
  mov esi, [ebp+12] ; Move value of parameter 2 into ESI
  mov edi, [ebp+16] ; Move value of parameter 3 into EDI
  mov [ebp-4], edi ; Move EDI into the local variable
  add [ebp-4], esi ; Add ESI into the local variable
  add eax, [ebp-4] ; Add the contents of the local variable
  ; into EAX (final result=sum of the three
  parameters)
(cont'd)

## Slide 81
  ; Subroutine Epilogue (收場)
  pop esi ; Recover register values
  pop edi
  mov esp, ebp ; Deallocate local variables
  pop ebp ; Restore the caller's base pointer value
  ret
_myFunc ENDP
(end)